# Expert-N NOAH Soil Types

## Material and Methods
The Expert-N NOAH Soil Types are essentially datasets taken from the SOILPARM.TBL (see below). To adapt the parameters for usage in Expert-N, specific conversion factor had to be applied.
### SOILPARM.TBL
These parameters are functions of soil-category index		Corresponding XN soil parameter	Unit	Conversion Factor (NOAH => XN)
BB	B parameter [-]	camp_b
DRYSMC	Dry soil moisture threshold at which direct evaporation from top soil layer ends [volumetric fraction]	res_water_cont		*100.0
F11	Soil thermal diffusivity/conductivity coefficient [units??] (Unused in Noah LSM?)
MAXSMC	Saturation soil moisture content (i.e., porosity) [volumetric fraction]	Porosity, / cont_sat	[Vol%]	*100.0
REFSMC	Reference soil moisture (field capacity), where transpiration begins to stress / [volumetric fraction]	field_capacity	[Vol%]	*100.0
SATPSI	Saturation soil matric potential [-]	camp_a	[-]	*1000.0
SATDK	Saturation soil conductivity [m/s]	cond_sat	[mm/d]	*1000.0 * 86400.0
SATDW	Saturation soil diffusivity [m/s]
WLTSMC	Wilting point soil moisture [volumetric fraction]	wilting_point	[Vol%]	*100.0
QTZ	Soil quartz content [units??]

Calculation of the bulk density according to equation 6 (Miller and White, 1998):
BD = (1-porosity)*PD
where
BD	… Bulk Density [g/m³]
porosity	… Porosity [-]
PD	… Particle Density [g/m³], assumed 2.65
## Literature
Miller, D. and White, R. A., A Conterminous United States Multilayer Soil Characteristics Dataset for Regional Climate and Hydrology Modeling, Earth Interactions V2, 1998
SOILPARM.TBL, Weather Research and Forecasting Model